## Slide 1
EPM-Series Power Meter(N1913/14A) Firmware Upgrade Process
Notes: <number>

## Slide 2: Hardware/Software Requirements
The current hardware requirements for this procedure are:
(a) A PC running Windows 2000® or Windows XP®.
(b) A GPIB interface card, LAN connection, or USB port.
The current software requirements for this procedure are:
(a) A VISA library (e.g. Agilent IO Libraries).
(b) The EPM-series Firmware Files for your instrument.
(c) The EPM-series Firmware Upgrade Application (FwUpdateApp.exe).
Note: This procedure has not been tested on other versions of Windows.
Firmware Upgrade
Notes: <number>

## Slide 3: Obtaining The Software
    The latest version of the Agilent IO Libraries can be obtained from the following link: Agilent IO Libraries
    The P-Series Firmware Upgrade Application can be obtained from the following link: EPM-series firmware upgrade
    Save the file to PC hard drive
    Note: This is a WinZip® executable file that must be unpacked before use.
    The EPM-series Firmware Upgrade Application is included in the WinZip® executable file (“FwUpdateApp.exe”)
Step 3 : Firmware Upgrade (Cont’)
Notes: <number>

## Slide 4: Firmware Upgrade Process
Step 1:
Run the ‘FwUpdateApp.exe’ application. This does not need to be installed – simply double-click on the file to run it.
Step 2:
Click on the ‘Browse’ button next to ‘Release Directory’, and select the directory
in which the firmware files reside.
Step 3:
Click on the drop-down arrow next to ‘VISA Instrument’, and select the unit to be
upgraded.
Note: This drop-down feature only works for upgrades over GPIB & USB. If the upgrade is being performed over LAN, then enter the IP address in this box.
Latest Revision
GPIB Address
Notes: <number>

## Slide 5: Firmware Upgrade Process
Step 4:
Click on the ‘Upgrade’ button.
Click ‘Yes’ on the warning pop-up when
asked about instrument saved states.
Notes: <number>

## Slide 6: Firmware Upgrade Process
Step 5:
A warning message to notify the
instrument’s saved state(s) will be erased.
Click ‘Yes’ to proceed with the installation.

## Slide 7: Firmware Upgrade Process
Step 6:
Click ‘OK’ on the pop-up that appears
when the upgrade is complete.
The power meter will take less than
5 minutes to complete the upgrade.
Now, the power meter will now
automatically execute a power cycle.
You have successfully upgrade the new firmware!
Notes: <number>